# Description

This kit contains the parts needed to make an LED scrolling message display. It comes in two formats: a kit where wires are soldered and a kit where all wires are plugged in.

# Parts List

1. ATMega328 microcontroller in breadboard (black ectangular)
2. Potentiometer (knob) with 3 wires
3. Push-button switch with 2 wires
4. LED Matrix in breadboard (square with 64 dots and 16 pins)
5. Battery holder (large rectangle with 2 wires)
6. Wires (mostly long and two short)
7. LED for testing

# Assembly Instructions
1. Find the breadboard with the microcontroller plugged into it. Look at the picture of the microcontroller. It has 28 pins numbered 1 to 28. We will be connecting wires to the various pins, so it is important to understand how they are numbered.
2. We will start by connecting the battery to the microcontroller and then testing to make sure it works. Position the microcontroller breadboard so that the microcontroller is at the top and some empty rows of holes is at the bottom. Use the two empty rows on the left side below the microcontroller. Plug the red battery wire into one row and the black wire into the other row. Make sure the battery wires are not connected in the same row, or the batteries will short and get hot when the switch is turned on. Make sure the switch on the battery holder is off.
3. Connect a short wire to the same row as the red battery wire. Connect the other end to pin 7 of the microcontroller.
4. Connect a short wire to the same row as the black battery wire. Connect the other end to pin 8 of the microcontroller.
5. To test the microcontroller, connect an LED between pins 13 and 14. It doesn't matter which wire goes where. Turn on the battery switch. You should see the LED flash periodically.
6. When you are done with the test, turn off the battery switch and leave the LED connected.
7. Next we will connect the potentiometer (knob) and test it. Connect the black wire of the knob to the same row as the black battery wire.
8. Connect the red wire of the knob to the same row as the red battery wire.
9. Connect the last wire of the knob to pin 28 of the microcontroller.
10. Turn on the battery. The LED should start flashing. Turn the knob. As you turn it, the flashing should speed up or slow down. This means the knob is connected correctly.
11. When you are done with the test, turn off the battery switch and leave the LED connected.
12. We will now connect the button and test it. Connect one wire of the button to the same row as the black battery wire.
13. Connect the other wire of the button to pin 27 of the microcontroller.
14. Turn on the battery switch. The LED should flash. Press the button once. The LED should stop flashing. It will either turn off or stay on, depending on where the knob is turned. Turn the knob to see if you can make the LED turn on and off.
15. When you are done with the test, turn off the battery switch and remove the LED.
16. It is now time to connect up the LED matrix. Make sure you have the 16 long wires and the LED matrix.
17. Take the wires. One end of the wires will plug into the pins of the LED Matrix. Carefully plug each wire to one of the LED Matrix pins, being careful not to bend the pins. When all of the wires are plugged in to the Matrix, push down on them to make sure they are tightly connected. Sometimes the wires get loose, so it is a good idea to tape around the bundle of wires close to the matrix to hold them tightly in the pins.
18. Plug the other end of the 16 wires on the Matrix into the mictocontroller. You will plug them into certain pins of the microcontroller listed here. It does not matter which wire goes to which pin. Carefully check that the wires are plugged into the correct pins on the microcontroller. Remember that you look down from the top to see the pin numbers, but the actual pins are on the under side of the microcontroller.
  4, 5, 6, 11, 12, 13, 14, 15, 16, 17, 18, 19, 23, 24, 25, 26
19. To keep the wires neat and tight, you can tape around them like you did with the matrix.
20. To test if the matrix is connected properly, turn on the battery switch. You should see all dots of the matrix light up. If the knob is turned one way, the dots will flash slowly. Turn it the other way and all the dots will light up.
21. If you have any dots that don't light up, there is a problem with the connections between the LED matrix and the microcontroller. Check the pin numbers and make sure the connections are tight.

1. We will now test if these wires are plugged in correctly. Make sure the switch on the battery holder is OFF. Plug the red wire of the battery holder into pin 7 and the black wire into pin 22 of the microcontroller.
2. Turn the battery switch ON (make sure you have batteries in the battery holder. You should see random dots flash on the Matrix. Make sure that all rows and columns of the matrix have flashing dots. If a row or column is not flashing, there is a problem with one of the wires.
3. Turn the battery holder switch OFF and unplug the two wires from the microcontroller.
4. Connect the yellow wires of the potentiometer (knob) to pin 27 of the microcontroller.
5. Connect the black wire of the potentiometer to one of the holes in the 4-hole connector.
6. Connect the red wire of the potentiometer to one of the holes in the 3-hole connector.
7. Connect one of the wires of the push button to pin 26 of the microcontroller.
8. Connect the other wire of the push button to one of the holes in the 4-hole connector.
9. Connect the red wire of the battery holder to one of the holes in the 3-hole connector.
10. Connect the black wire of the battery holder to one of the holes in the 4-hole connector.
11. Connect a wire from pin 7 of the microcontroller to the last hole in the 3-hole connector.
12. Connect a wire from pin 22 of the microcontroller to the last hole in the 4-hole connector.

# Configuring the Display
When you plugged the pins into the LED Matrix, it didn't matter which pins you plugged the wires into. This means that the display does not know which pins go to which LED. It also doesn't know which direction the electricity needs to flow to make the LEDs light. You need to perform a few steps to tell the display these things. You only have to do this once, unless you take the pins out and put them in again.

## Random Dots
Remember when you turned the display on before with just the battery holder and LED Matrix connected? The display produced electricity in both directions between all of the pins, not knowing which pins would connect to the various LEDs. This caused random LEDs to light up when one of the connections happened to work.
If the potentiometer was connected properly, you can turn it one way and the random dots will speed up and the other way and they will slow down. If nothing happens, there is a problem in the wiring or the potentiometer.
If you press and release the push button, the random dots will disappear and you should see a line on the LED Matrix.
## Random Liness
As you turn the potentiometer, will will see random lines on the Matrix. Some will be horizontal (a row) and some will be vertical (a column). This is the display trying to send electricity from one of the pins to all the other pins very quickly in both directions.
Position the Matrix so that it is steady and decide which edge will be the top. Once that is done, it's time to start telling the display which pin does which row or column.
Turn the potentiometer until the first column lights up. That is the leftmost line of LEDs. Press the button. The line will flash and go out. The display now knows which pin is for column 1.
Repeat this for the next column over from the left. This is column 2. Press the button. Repeat this until all 8 columns have been entered.
Now do the same thing for the rows, starting with the top rows. Enter in all 8 rows.
## Random Liness
After all 8 columns and rows are entered and the button is pressed for the last time, you should see either 1 or 2 dots light in the top row. You now need to tell the display which direction the electricity needs to flow to light up a column. The left dot has electricity going both ways, so it always lights up. The next dot has electricity flowing one way if the knob is turned to the left and the other way if it is turned to the right. Turn the knob until you see 2 dots light up. Then press the button.

## Brightness Calibration
The brightness of the LEDs is controlled by how long they remain on as they are displayed. The display can only show one column at a time, so each column is briefly turned on and then off before displaying the next column. The longer the column remains on, the brighter it becomes. But if the column remains on too long, the display will flicker because it takes too long to display all the columns.
You want to control the brightness so that it is bright enough to see but not so bright that it begins to flicker.
You shoud see a dot in the left center of the Matrix. You turn the knob to adjust how bright the display will show 1 LED. Choose a brightness in the middle. Press the button.
You will now see 2 LEDs displayed above the 1 LED. You need to adjust the brightness of the 2 LEDs so that it matches the 1 LED. As you add LEDs, the brightness decreases because it takes more power to light them and that causes them to glow dimmer. You may need to adjust the knob slightly to make the 2 LEDs as bright as the 1 LED. Press the button.
Repeat this process as the number of LEDs incresses to 8. As the LEDs increase, they need to remain on longer to be as bright as 1 LED. If you get the LEDs as bright as they can get, but they are still not as bright as the 1 LED, you made the 1 LED too bright. You can reconfigure the brightness. Continue adjusting the brightness until the line of 8 LEDs is done.
## Hello World
After you have configured the last brightness line and press the button, the display will show a scrolling message that says "HELLO WORLD". You can adjust the knob to change the speed of the scrolling message.
## Changing the Brightness
If the display flickers, or if you don't like the brightness levels you configured, you can reconfigure the brightness. To do this, turn the switch off on the battery holder. Before turning it on again, hold the button in. Turn on the switch and hold it for a second and let go. You should see one dot. If you see random dots, you held the button in too long. In that case, turn the switch off and try again. If you see the message scrolling, you did not hold in the button long enough. Try again.
## Reconfiguring the Pins
If you remove the pins from the LED Matrix, or if the display looks wrong, you can configure the pins like you did when you first started. To do this, turn off the battery switch, hold the button in, and turn on the battery switch. Hold the button for 5 seconds and let go. You should see random dots. If not, try again.
## Entering Your Own Message
You may enter your own scrolling message, up to approximately 200 letters and spaces. Do the following while the display is on and scrolling the HELLO WORLD message.
1. Hold in the button for 5 seconds and release. You should see a letter displayed on the Matrix. If not, turn the potentiometer. As you turn the knob, you will see all the letters of the alphabet along with a space and an arrow.
2. Turn the knob until the first letter of the message is shown. Press the button. The letter will flash, indicating that it was entered.
3. Continue with the next letter or space of the message. Enter as many characters as desired, but do not enter the arrow.
4. When you are done entering the message, turn the knob until you see the arrow and press the button. This tells the display that the message is done. You will see the message scrolling across the Matrix. Turn the knob to change the speed of the scrolling message.
## Display Memory
The display has a permanent memory that holds the message and configuration information, even when the battery is turned off or disconnected. That means you will not lose your message when you turn off the display. This also means that if you take apart the display and later put it back together, it will still have the pin configuration of the last time you put it together. The display will not work, and the most you will see is random dots as the old message scrolls. It is important to remember to reconfigure the display after the pins of the Matrix are reconnected.